## Slide 1
ClickSend
Service
IFTT
Service
PwrMonitor: Block Diagram
GKE Dec 25th, 2019
House
Electrical
Panel
4x(RMS Converters & ADCs)
Analog
Measurements
(Voltage, Current, Phase Factor)
Phase #1 (V1, I1, ph1)
Phase #2 (V2, I2, ph2)
RS-485
RS-232
2 x RS485
interfaces
2 x PZEM-16
NodeMCU
Processing
& WiFi
publishingv
Sec RS232
interface
RF 433MHz
Pri RS232
interface
USB
RF 433MHz
USB
This Photo by Unknown Author is licensed under CC BY-SA
Thinger.io
IoT Service

## Slide 2
myGlobals.cpp
Defines & exports:
Global::myp
Allocates & exports:
NMP nmp
myCliHandlers.cpp
Exports:
mypTable[ ]
Allocates (used locally only):
CLI :: cli
EXE::exe
EEP::eep
BUF::buffer
TICsec::pr, streamTic
PROF::prof
PwrMonitor.ino setup() and loop()
myThinger.cpp
Exports:
THING_STREAM()
THING_HANDLE()
notifyViaIFTTT()
sendtoDropbox()
mgnClass.cpp
L1 Library
cpuClass.cpp
bufClass.cpp
cliClass.cpp
eepClass.cpp
nmpClass.cpp
ticClass.cpp
mgnClass.cpp
externIO.h
L2 Library
OneWire.cpp
ds18Class.cpp
SimpleDHT22.cpp
externIO.h declares:
cpu
cli
exe
eep
server
GKE Dec 2nd, 2019
CommonCLI.cpp (in Lw)
Exports:
cmnTable[ ]
inkParms2cmnTable()
myEngClasses.cpp
Defines & exports:
PZENG::eng
VWSTATS::shortT, longT
ALARM::alm
TMBASE::tmb
TOCsec::ticMin, ticHr
Allocates & exports:
CPU cpu
OLED oled
PZ16 pz( cpu, oled )
SimpleSTA.cpp (in Lw)
mySupport.cpp
TICsec::secTic
reportVAP()
isSimulON()
isNotifyON()
setAnyMegParm()
setAnyEEParm()
getAllState()
showMegAllParms()
readSimulPhase()
getSimulPhase
refreshState()

## Slide 3
setup()
Init OLED
Init Parms
Init CLI Tables
Wait for RETURN or BUTTON
Setup WiFi
Setup OTA
Setup Thinger
Setup EEPROM parameters
stdLoop()
Handle OTA
On cli ready,
  Handle CLI
On secTic,
  Read phases #1 & #2 alternating
  Compute short term stats
  Compute long term stats
  Check for Alarms
If WiFi OK
  Send to Dropbox periodically
  Check for alarms
    Send notifications
  Handle Thinger
Else
  Reconnect WiFi
Measurements
vap[1]
Vap[2]
Vap[1+2]
Statistics
Vmin
Vavg
Wavg
Wmax
kWh
Thinger
Cli Handlers

## Slide 4
NodeMCU
D1-GPIO5-SCL
D2-GPIO4-SDA
D6-GPIO12-SEN
D7-GPIO13-RxD
D8-GPIO15-TxD
RxD-GPIO13
TxD-GPIO15
OLED
SCL
SDA
GND
VCC
TXS101
OE
GND
A1
Va
A2
G
GND
B1
Vb
B2
3.3v
3.3v
RS485
Vcc
RxD
TxD
GND
B-
A+
GND
3.3v
OR-’32
B
A
GND
Vcc
Y
3.3v
TXM
433MHz
3.3v
TxD
SET
GND
RxD
Vcc
Wiring Diagram
PwrMonitor
GKE Nov 30th, 2019
OR’ Gate
IF A=LOW, Y=TxD
IF A=HIGH, Y=HIGH
SecondaryUART
To enable, set SEN (A) HIGH